HW overview
HW overview
24VDC
(supply)
15 wires:
6xPWM,
Fault, Wake, Engate,
4xSPI,
DcBusVoltage,
GND
BOOSTXL-
DRV8305EVM
(bridge driver with mosfets)
BOOSTXL-
DRV8305EVM
(bridge driver with mosfets)
BLDC
(e-machine)
ESP32
(mcu)
3 wires:
U, V, W
Hall signal
circuit board
5 wires:
HallA, HallB, HallC, 3.3V, GND
5 wires:
HallA, HallB, HallC, Hall+, Hall-

---
SW overview 1
SW overview – part 1
Task1ms:
- MeasDcBusVoltage
- PidControl
Task10ms:
- UartSend
- UartReceive
Task100ms:
- SpiSendReceive
Core0
- Task1ms
- Task10ms
- Task100ms
Core1
- Main loop()
- isr callback()

---
SW overview 2
SW overview – part 2
MeasDcBusVoltage:
ADC measurement of dc bus voltage. Convert to physical value. Check if within valid range (22V-25V), in case out of range switch to state error.
PidControl:
Controls the duty cycle of pwm signals to reach desired rpm
UartSend:
Sends following data via uart: state(idle, run, error), dc bus voltage, current rpm, current duty cycle, status register DRV8305
UartReceive:
Receives following commands via uart: „1“ (start motor), „4“ (stop motor), „n=xxxx“ (desired rpm in range 1000-5000)
SpiSendReceive:
Checks status register of DRV8305